| TABLE NO | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EXAMPLE ORDER NO 101 | K |  | 2 |  | 3 |  | 018 |  | U |  | M |  | P |  | 0100 |  | S |

Example Order No. = Type  101  T/C-K ; 1/8” sheath diameter ; Inconel 600 sheath material ; 18” long ; ungrounded measuring junction ; 1/2"  N.P.T connection ; PVC cable ; 100 mm cable length ; standard calibration.

| Table 1. Sensor Type |  | Table 2. Sheath Diameter “D” |  | Table 3. Sheath Material |
| --- | --- | --- | --- | --- |
| Single | Duplex |  | Order | Diameter |  | Order | Description |
| K | KK |  | 1 | 1/16” |  | 3 | Inconel 600 |
| J | JJ |  | 2 | 1/8” |  | 4 | 310 ST.ST. |
| T | TT |  | 3 | 3/16” |  | 8 | 316 ST.ST. |
| E | EE |  | 4 | 1/4" |  | 9 | 304 ST.ST. |
| N | NN |  | 6 | 3/8” |  |  |  |
| P (for RTD) | PP |  | 7 | Other |  |  |  |
| Table 4. Dimension “U” |  | Table 5A. Measuring Junction (for T/C only) |  | Table 5B. Wiring System (for RTD’S only) |
| Insert “U” in inches. ( 3 digit ) |  | Order | Description |  | Order | Description |
|  |  | G | Grounded |  | 2 | 2-wire system |
|  |  |  | U | Ungrounded |  | 3 | 3-wire system |
|  |  |  | E | Exposed |  | 4 | 4-wire system |
| Table 6. Process Connection |  | Table 7 Cable Type * |  | Table 8. Cable Length |
| Order | Description |  | P | PVC |  | Insert “L” in mm. |
| M | 1/2“ N.P.T |  | T | Teflon-TFE |  |  |
| R | 1/2" B.S.P |  | G | Glass Fiber |  | Table 9. Sensor Accuracy |
| Q | 3/4" N.P.T |  | S | Silicon Rubber |  | Order | Description |
| V | 3/4" B.S.P |  | GS | Glass Fiber + Metal Overbraid |  | S | Standard |
| O | Other |  |  |  |  | SC | Special Calibration |

* For additional armor tube add an “AR” to cable type.

# Text boxes

## HOW TO ORDER

TYPE 101

Type 100 is a standard sensor suitable for use with basic applications.

Type 100 is available in

a variety of features and options to meet users' specific requirements, including:

- Sensor Type

- Sheath Diameter

- Sheath Material

- Length

- Cable Length

- Sensor Accuracy